## Slide 1
IILM University
Greater Noida, U.P.
School of Computer Science
& Engineering
INTERNSHIP PRESENTATION • 2026–27
2nd Year, 3rd Semester | B.Tech CSE
Organisation: MARS Group
AI-Assisted Marine Risk
Intelligence &
Community Reporting
Platform
Student Name:
NAVNEET KUMAR
Roll Number:
25SCS1003003086
Program:
B.Tech CSE — Sem 3
Organisation:
MARS Group

## Slide 2
Project Overview
AI-Assisted Marine Risk Intelligence & Community Reporting Platform | NAVNEET KUMAR | IILM University
2
What We Built
A geospatial marine intelligence system that fuses satellite sea-surface temperature (SST) data, community-reported coastal incidents, and simulation tools to identify at-risk marine zones and support early environmental response — designed for use by NGOs, coastal authorities, and researchers.
Data Ingestion
Satellite SST from NOAA, OISST, NCEI & OceanSODA
+ Ocean chemistry (pH, salinity, CO₂)
SST Anomaly Engine
Anomaly = Current SST − Historical Mean
1991–2020 climatology baseline
GIS Risk Mapping
QGIS + PostGIS spatial layers
IDW interpolation & risk zone classification
Community Platform
Field incident reporting
Auto-verified against computed risk zones

## Slide 3
Problem Statement
AI-Assisted Marine Risk Intelligence & Community Reporting Platform | NAVNEET KUMAR | IILM University
3
01
Rising Ocean Temperatures
Sea-surface temperatures are increasing at unprecedented rates, causing mass coral bleaching, species migration, and habitat destruction across global marine ecosystems.
02
Data Accessibility Gap
Existing satellite monitoring systems require highly specialised expertise, leaving coastal communities and NGOs without actionable real-time intelligence.
03
Fragmented Data Sources
Critical datasets (SST, pH, salinity, CO₂) exist in isolated silos with incompatible formats and coordinate conventions, making integrated analysis nearly impossible.
04
Delayed Environmental Response
Without early warning tools, environmental agencies react after damage occurs rather than before, significantly reducing the effectiveness of conservation interventions.

## Slide 4
Project Objectives
AI-Assisted Marine Risk Intelligence & Community Reporting Platform | NAVNEET KUMAR | IILM University
4
01
Ingest & process satellite SST data from NOAA, OISST, NCEI, and OceanSODA
02
Compute SST anomalies against a 1991–2020 historical climatology baseline
03
Render interactive GIS layers: SST values, anomaly maps, and risk zones
04
Simulate marine heatwave spread and spatial impact for decision-makers
05
Enable community reporting of coastal pollution with automated risk-zone verification
06
Build a multi-parameter risk model integrating SST anomaly, pH, salinity, and CO₂
07
Deliver an interactive dashboard for NGOs & coastal environmental authorities

## Slide 5
Technologies & Tools Used
AI-Assisted Marine Risk Intelligence & Community Reporting Platform | NAVNEET KUMAR | IILM University
5
Data Processing
Python · Pandas · NumPy · Xarray · NetCDF · CSV
Geospatial Analysis
QGIS (EPSG:4326) · IDW Interpolation · PostGIS
Database
PostgreSQL · PostGIS · pgAdmin · Prisma ORM
Backend
Node.js · REST API · Python–PostgreSQL Pipeline
Frontend / Dashboard
Streamlit · Plotly Express · Responsive Web Design
Data Sources
NOAA · OISST · NCEI · OceanSODA

## Slide 6
My Role & Responsibilities
AI-Assisted Marine Risk Intelligence & Community Reporting Platform | NAVNEET KUMAR | IILM University
6
Primary Role: DATA COLLECTOR & HANDLER
Data Collection & Research
Identified & compared NOAA, OISST, NCEI & OceanSODA satellite datasets by resolution, coverage, and quality
Data Cleaning & Validation
Removed duplicates, missing values & invalid coordinates; standardised formats across all heterogeneous sources
SST Anomaly Computation
Implemented anomaly formula (Current SST − Historical Mean) and validated against NOAA reference maps
Geospatial Optimisation
Resolved longitude bug (0–360° → −180°/+180°); aggregated 0.25° to 10° grid for GIS performance
Ocean Chemistry Integration
Processed pH, salinity, CO₂ parameters and integrated them into a multi-parameter marine risk framework
Cross-Functional Coordination
Collaborated across 8-member team: GIS, DB, Backend & Frontend engineers, plus comprehensive documentation

## Slide 7
Methodology — 8-Step Pipeline
AI-Assisted Marine Risk Intelligence & Community Reporting Platform | NAVNEET KUMAR | IILM University
7
01
Data Collection & Research
02
Data Cleaning & QA
03
Coordinate Normalisation
04
SST Anomaly Computation
05
Multi-Parameter Risk Framework
06
Geospatial Optimisation
07
Backend Integration & Testing
08
Dashboard Support

## Slide 8
Key Contributions & Challenges
AI-Assisted Marine Risk Intelligence & Community Reporting Platform | NAVNEET KUMAR | IILM University
8
Key Contributions
✓
Built the foundational SST & ocean-chemistry dataset relied on by every downstream module
✓
Resolved critical longitude convention bug (0–360° → −180°/+180°) for all GIS coordinate work
✓
Designed the multi-parameter marine risk framework grounded in peer-reviewed literature
✓
Served as cross-functional bridge between data science and engineering teams
✓
Delivered comprehensive documentation enabling future pipeline maintenance & scalability
Challenges & Solutions
⚠ Longitude Mismatch
→ Transform rule: IF Long > 180, Long − 360, verified against NOAA maps
⚠ Over-Cleaning Risk
→ Incremental cleaning with team review of statistically uncommon but valid readings
⚠ Grid Resolution
→ Tested 1°, 5°, 10° — selected 10° optimal balance of accuracy & performance
⚠ Multi-Parameter Model
→ Literature review — model grounded only in scientifically supported relationships

## Slide 9
System Architecture
AI-Assisted Marine Risk Intelligence & Community Reporting Platform | NAVNEET KUMAR | IILM University
9
1 Data Ingestion
NOAA · OISST · NCEI · OceanSODA (NetCDF / CSV)
2 Data Processing
Python — Pandas · NumPy · Xarray · Anomaly Engine
3 Geospatial Layer
QGIS · PostGIS · IDW Interpolation · WGS 84
4 Backend / API
Node.js · REST API · PostgreSQL / PostGIS · Prisma ORM
5 Presentation
Streamlit Dashboard · Plotly Express · Community Reports

## Slide 10
Learning Outcomes
AI-Assisted Marine Risk Intelligence & Community Reporting Platform | NAVNEET KUMAR | IILM University
10
📊
Data Quality is Foundational
Every downstream module depended on clean, validated data. Poor quality would have cascaded across the entire platform.
🤝
Communication is Critical
Working across 8 specialisations required clear documentation, early coordination, and translating technical decisions clearly.
🔬
Science Matters in Engineering
Grounding the risk framework in peer-reviewed marine literature made outputs more robust and scientifically credible.
🔄
Iteration is Essential
Best results emerged through testing, validation, and refinement — not from getting everything right on the first attempt.
🌊
Real-World Impact
Building tools for NGOs to monitor ocean health and respond to marine crises made the technical work deeply meaningful.
⚙️
End-to-End Pipeline Thinking
Designing for scalability, reproducibility, and handoff — not just correctness — is what makes production-quality software.

## Slide 11
IILM University
School of Computer Science & Engineering
B.Tech CSE | 2nd Year, 3rd Sem | 2026–27
Thank You
This 45-day internship delivered a production-ready geospatial marine intelligence platform — from raw satellite telemetry to an interactive risk dashboard — demonstrating the real-world power of data science in environmental conservation.
NAVNEET KUMAR
Roll No: 25SCS1003003086
Organisation: MARS Group
Questions Welcome